## Slide 1: Adaptive Effort Classifiers: A System Design for Partitioned Edge/Cloud Inference
Divya Sankar
Advisor: Ravindran Kaliappa

## Slide 2: Inference on Edge/Cloud Systems
Data captured by the edge device is wirelessly transmitted to the cloud for advanced data processing
  E.g. Cameras used in surveillance.
Edge devices are usually energy-constrained as they are battery-driven systems
  Most of the energy is consumed in data sensing and transmission
  Severely limits application scope
Edge Device
LTE / WiFi
Data captured by sensors on the device
Information processing through sophisticated algorithms
Wireless transmission to the cloud
Cloud

## Slide 3: Embedding Intelligence at the Edge
Add intelligence on the edge device to reduce sensing/transmission energy
  Sense data with low fidelity and apply ML to understand its significance
  Gauge when interesting events occur and selectively sense and transmit
(2013)
*https://wiki.ubuntu.com/Specs/M/ARMSoCOMAP?action=AttachFile&do=get&target=OMAP_Overview_UDS.pdf
(2012)
(2014)
(2014)
(2014)
However, implementing state-of-the-art ML algorithms directly at the edge is also challenging
  E.g. Deep Neural Networks that provide the highest classification accuracy takes few giga ops to classify a single image
    Do not fit within the resource constraints at the edge
Sensor
ADC
Tx
Edge-ML
Cloud Processing
LTE / WiFi
Rx
Goal: New resource-efficient classifier for partitioned edge/cloud inference engine!

## Slide 4: Adaptive Effort Classifiers: Motivation
Insight: Inputs differ greatly in their inherent classification difficulty
  Most inputs lie away from decision boundary & easy to classify
  The small fraction of inputs that lie close to the decision boundary require the full effort of the classifier
ML-classifiers are fixed-effort systems  Same model for all inputs
  Leads to inefficiency when high accuracy is not needed
  (full model generates unnecessary data transmissions and/or processing)
Feature 1 
+
Feature 2 
-
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
Chart: Class probability (dist. from decision boundary) 
Easy-to-classify
inputs
Hard-to-classify inputs
95%
70%
MNIST
Easy inputs
Easy inputs
Decision
Boundary
Notes: The key motivation for our works stems from the observation that inputs to classifiers vary in their inherent classification difficulty. We illustrate this using a simple example. Figure shows the inputs in a 2-class classification problem. The class labels are + and -. The points are spread in a 2 dimensional input feature space; classifiers typically learn a decision boundary as shown to distinguish the classes. The key insight Is that majority of the inputs lie far away from the decision boundary and intuitively do not need the full complexity of the classifier. Whereas, the small fraction near the decision boundary require its full effort. We quantitatively illustrate this using the MNIST handwritten digit recognition dataset. Figure shows the distribution of class probabilities of inputs for the dataset when a support vector machines classifier is used. We find over 70% lie far away from the boundary and are classified with a class probability of over 0.95. Some representative easy and hard inputs are shown.
While inputs vary in difficulty, ML classifiers are fixed effort systems.. i.e. the same classification model is used on all inputs thereby spending equal, in fact worst-case, effort on all. Clearly this leads to significant inefficiency and we address this problem by proposing scalable-effort classifiers.

## Slide 5: Adaptive Effort Classifiers: Concept
Adaptive effort classifiers modulate computational effort across inputs
  System constraints (e.g. battery) can also be considered to modulate effort
Chain of classifiers of growing accuracy and complexity
  Each stage classifies an input (or) passes to next stage
Initial stages of the adaptive effort classifier realized on the edge; more complex final stages execute on the cloud
Stage N
Stage 1
Stage 2
Don’t know
Input
Class
Output
?
?
Yes
Don’t know
Yes
Easy inputs  Low effort
Hard inputs  High effort
Notes: The key idea behind SE classifiers is they adapt the effort expended based on the difficulty of the inputs. Instead of a single complex model, SE classifiers are designed with a chain of models of growing complexity and accuracy. Each stage in the chain is equipped to gauge the difficulty of the input; and either classify the input or pass it to the next stage. So, the easy inputs are classified by the initial stage with very low effort, while the difficult inputs are passed through the chain. The final stage is similar to the original classifier and classifies all the inputs. Thus scalable effort execution is achieved by expending effort commensurate with the difficulty of the inputs

## Slide 6: Adaptive Effort Classifiers: Design
Identify knobs that can scale the effort of classifier to meet the timeliness and accuracy constraints [T,A] on the object/event inference
Idea1: Classifiers with progressive feature set
  A small number of important features are used in the initial stages
    E.g. Use a sampled image, employ PCA
  A complex classifier uses the complete feature set
  In surveillance, threat perception can determine choice of feature sets
  Zoom in/out on a target, by dynamically adding/deleting features to the classifier
  Increase of feature set  Needs more processing cycles & battery energy, increases time to decide
Idea2: Classifiers with progressive data bit width
  Modulate the computational representation of {(feature, value)} sets
  Initial classifiers can operate with low bit-level precision (say, 4-8 bits); more complex classifiers may increase data bit-widths
  Precision used in computations is orthogonal to the choice of feature sets

## Slide 7: Datasets
For proof-of-concept, we will start with small datasets such as
MNIST
CIFAR-10